If you own a Fuji 3D camera W1/W3, and you want to present your 3D works to the public at an exhibition or at a party of family/friends getting together, the ProMa 3D Player MV is a perfect tool for this job.

Other than the ProMa 3D Monitor Pro, this ProMa 3D Player MV is designed to showcase 3D photo and video works to multi people watching simultaneously without wearing glasses. Best watching angle is about 45° to each side.

Now, how to display your 3D works from Fuji W3?

1,  Take out SD card from your Fuji W3 camera, and put it into an USB adaptor.

2, Plug your USB adaptor into a computer and open a mpo photo by Adobe Photoshop.

3,  While open the mpo photo, there would be a question window asking to create 3D layers, Click YES.

4,  On the right size, there is a selection for the 3D type (format), you select Side By Side. If your 3D photo is 16:9's, it would be right way to convert into Half SBS 3D. If your 3D photo is 4:3’s, you need to adjust the center position of left and right image to be centered in the left and right.

Half SBS 3D photo, perfectly to play at ProMa 3D Player MV

Full SBS 3D photo, incorrect to play at ProMa 3D Player MV, long side would be prolonged.

5,  Once it shows the side by side 3D, you save the photo. Press "Save As", then it will ask for the file name, you can put in the file name with suffix as xxxxx_2V3D, also you need to select the photo format as .jpg, so that your monitor would play it automatically.

Save as: it is to save the photo as another file without over write your original .mpo file, which is still there.

Save: is to save the file as over write the original file.

6,  Once you finish the photos you want, then you can take out the USB, and plug into the ProMa 3D Player MV, then the photos would be uploaded and played automatically.

(You do not mind the original mpo files in the USB, they would not be uploaded to the player, as the player does not recognize them.)

Notice:

1,  The ProMa 3D Player MV would automatically recognize and play the file formats as its suffix:

Side by Sid 3D name as:  xxxxx_2V3D

Up and down 3D name as:   xxxxx_TB3D

9 tile 3D name as:  xxxxx_MV3D

2D to convert into 3D name as:  xxxxx_1V3D

2,  For 3D photos, you can setup the photo play time in the menu as 5 secs, 10 secs etc.

Steps: On the remote control, press button Setup >> System Control >> Play Time >> Select the play time you want and press OK.